## Slide 1: P&D: Speech5

## Slide 2: MATLAB
Flexible
  Structure easily changeable
    but if asymmetrical: account for delay
  Parameter definitions grouped in scripts
    changing and testing new parameters easy
Originally: input scaled to full 16bit range
  ↔ now: not for consistency with C

## Slide 3: Parameter choices
Tuneable parameters:
  Scalings
    Analysis
    Synthesis
     Trade-off clipping ↔ SNR
  Phi values
  Mu values
  Stop band attenuations
  Filter lengths
  Maxima  #bits

## Slide 4: Parameter tuning
Preprocessing:
  Files changed to 8kHz
    Audacity
    70dB decimation filter
Based on PESQ only
  More representative of human hearing system
  Maximizing equally weighted score of:
    Words_f, words_m, f116, f216, m116, m216, belasting, bir

## Slide 5: Parameter tuning
Modus operandi:
  Per band
  Manually greedy approach:
    Optimize parameter 1, then 2, then 1 again …
  Scaling massive impact
  Bufferlenghts:
    Large impact in lowest band
    Small in others
  Phi and mu values in higher bands small impact
  #bits:
    5,4,3,0: Using bits in the highest band is not worth losing them in another band

## Slide 6: Parameter tuning: results
Inherent filterdelay
  = 64/8000 + 32/4000
  = 16 ms
PESQ/SNR:
Final parameters:

## Slide 7: C
↔ MATLAB:
  Less flexible
    Structure hardcoded
    Parameters not grouped together
    Filters hardcoded
  Execution order:
    Buffer per buffer
    Keep history between calls
  Not scaling input (don’t know max value a priori)
     Removed in MATLAB

## Slide 8: C
Changes made for consistency C – MATLAB:
Notes: Vermeld: uiteindelijk ook integer ipv long long gedrag maar maakt geen verschil

## Slide 9: C
Preparing for crypto:
  Compress en decompress functions:
    30 shorts 15 bytes
    No bits wasted at all
  Buffer to crypto: 15*40= 600 chars
    Delay: 100ms
Notes: Vermeld: uiteindelijk ook integer ipv long long gedrag maar maakt geen verschil

## Slide 10: C
Performance measures
  In-place functions
  Profiling and optimization before DSP sessions!
    Speed-up x2
    Visual studio profiler
      Bottleneck: convolve: only nested loop + most calls + largest numbers

## Slide 11: C

## Slide 12: C: problems
Debugging:
  Gedit  Visual Studio / CodeBlocks
Output checked with MATLAB
  Results are the same down to the last bit

## Slide 13: DSP-C
Start: 21,8M cycles for 2986 samples
  After original x2 speed-up in C

## Slide 14: DSP-C: major improvements
Convolve:
  Left and right together  8%
    Hypothesis
      more freedom for compiler
      Overhead only once
  Long long  int: 49%
    Changed in MATLAB: no difference
   convolve no longer bottleneck
Notes: Percentages op totaal en niet op de aangepaste functie

## Slide 15: DSP-C: major improvements
(de)quantize:
  Smaller variable types: 42%
  Rewrote divisions: 38,5% on (de)quantize
    Binary/linear
   eliminates function calls
  Hypothesis: enables software pipelining of outer loop
Notes: Percentages op totaal en niet op de aangepaste functie Removed because mentioned later:
Test inline:
  Synthesis+analysis fully inlined:
    300k better (~5%)
    At this point not worth it
      Reverted for space and readability/manageability

## Slide 16: DSP-C: major improvements
Notes: NU WEL PER FUNCTIE

## Slide 17: DSP-C: major improvements
Convolve:
  Division as shift: 46% on convolve
   eliminates function call
  Original:
    Division for roundig to zero
  New:
    Complex division as shift for rounding behaviour+speed
Notes: NU WEL PER FUNCTIE

## Slide 18: DSP-C: major improvements
Convolve:
  Removed modulo in output index: 11% on convolve
Combine:
  Removed modulo in indices: 68% on these 2 functions
Rewriting divisions + removing modulos:
  Overall gain: 39%
(de)quantize:
  Combine left/right: 11%
 3,2M
Notes: NU WEL PER FUNCTIE

## Slide 19: DSP-C: major improvements
 Total results:
  Speed-up: 21,8M  3,2M
    = 85% or speed x 6,8
    Including original x 2: 13,6
Cheating mono input(?):
  Mono implementation:
    As long as input is mono:
      (de)quantize only one channel & copy
       2,7M (16%)
      At expense of slightly more code (2% of space)
Notes: TERUG OP TOTAAL
Trg vermelden: more compiler freedom (and reduced overhead)

## Slide 20: DSP-C: other improvements
Hardcoding filter coeffs in code
Must_iterate, unroll pragmas
Data_align: no noteworthy gain
Some intrinsics e.g. _abs
‘near’/‘const’ variables
Some function inlining
Inlining analysis/synthesis: 300k gain,
  Reverted for cleanliness & space
Notes: Removed: (Did not find it necessary to put this here since overall we implemented this and it did gain
UNROLL:
  Only really helped in convolve (4x best)
Removed: (Don’t understand this) Looked for intrinsics:
  did not help:
    Parallel on on cord (subword) instead of on two cores
    (might be better for P though)

## Slide 21: DSP-C: summary
Including initial x2: x13,6 gain
   1,071 cycles/sample
Bit/bit correct output
   guaranteed same PESQ scores as in MATLAB:
     parameters still easily testable